## Slide 1: Timeline
DATE | TOPICS | RELATED TOPIC
05/5/2025 – 09/5/2025 | Basic transformations: Negative, Power Law, Log, Piecewise Linear stretching, Thresholding. Histogram analysis: Histogram Equalization, Histogram Matching, Contrast Local Adaptive Histogram Equalization. | Basic transformations & Histogram analysis
12/5/2025 - 16/5/2025 | Correlation and Convolution, Box filter, Gaussian Filter, Median filter. Resize images, Nearest Neighbor Interpolation, Linear Interpolation, Bilinear Interpolation. | Fundamentals of Spatial filtering
19/5/2025 – 21/5/2025 22/5/2025 – 23/5/2025 | Sobel filter: Derivative in detecting edge, Gradient, Sensitivity of derivatives to noise, Sobel Filter Program Bilateral filter: Compare Bilateral Filter and Gaussian Filter, My implementation program | Sobel filter Bilateral filter
26/5/2025 – 28/5/2025 29/5/2025 – 30/5/2025 | Canny edge detecting: Gradient, Non-Maximum Suppression, Hysteresis threshold, My implementation program Morphological Image Processing: Dilation, Erosion, Opening, Closing | Canny edge detecting, Morphological Image Processing
02/6/2025 – 04/6/2025 04/6/2025 – 06/06/2025 | Morphological Image Processing: Hit or miss transform, Boundary Extraction, Thinning, Skeleton. Thresholding | Morphological Image Processing Thresholding
09/6/2025 – 11/6/2025 12/6/2025 – 13/06/2025 | Template Matching Hough Transform: HoughLines, HoughCircle | Template Matching Hough Transform

## Slide 2
HOUGH TRANSFORM

## Slide 3: Introduction
Image
Result of Canny Edge detection
T1 = 50, T2 = 150
Objective: find the two wheels of the bicycle, which can be described as circles
Challenge:
Extraneous data: Which point to fit to the circle
Incomplete data: Only part of the model is visible
Noise
Solution: Hough Transform
Notes: We can see the circles in the edge map, but we also see lots of other stuff
In the case of the bicycle, not all edges on the two wheels have been detected, creating some large gaps between the detected edges
Finally, we have noise — some of the edges on the wheel may be detected away from the wheel, and there may be other edges close to the wheel that do not correspond to the wheel
The Hough transform, gives us a powerful way to deal with these three problems in one shot. It works very well for simple shapes that can be described using a small number of parameters

## Slide 4: Line detection
Task: Detect line
y = ax + b
a: slope
b: y-intercept
Consider point (,
= a + b b =
x-y space
Notes: Let take a look at how HOUGH TRANSFORM work with the simplest shape, the straight line. Here we have a set of edge in a image. Embedded in the set of eged are any blue point that lie on a straight line. Our goal is to find this line. The line equation is …. If we consider a point on the straight line, example …. We can write …, since xi and yi are known we can rewrite this to a straight line equation in the ab space here. It illustrates all the line pass through the point xi yi when the parameter a and b vary. This concept allow us to consider the problem in 2 space. One is the image space and one is parameter space.

## Slide 5: Hough Transform concept
(, b
(,
= a + b
b =
(,
Image space
Parameter space
Point
Line
Line
Point
Notes: We will explore how the hough transform find the line in the image space by consider parameter space
So it is very interesting how there thing work out in image space and the parameter space
A point in image space maps to a line in parameter space, while a line in image space ends up as a point in parameter space. Based on this observation, we can create an algorithm to detect straight lines

## Slide 6: Multiple line detection
Image space
Parameter space

## Slide 7: Line Detection Algorithm
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
a
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
Step 1: Discretize parameter space (a, b) using a resolution that suits our application
Step 2: Create accumulator array A(a, b) to represent the discrete parameter space.
Step 3: Initialize the accumulator array with all values set to 0
Step 4: For each edge point , ):
A(a, b) = A(a, b) + 1
If (a, b) lies on the line: b =
Step 5: Find local maxima in A(a, b)
Accumulator array
Image
Notes: Consider all discrete values of a. For each value of a, a corresponding value of b that satisfies the equation b=−axi+yib = -a x_i + y_ib=−axi​+yi​ will be obtained. After finding the value of b corresponding to the value of a, increment the cell at coordinates (a, b) by 1.
The result obtained, as we can see, is a straight line in the parameter space. Where the two lines in parameter space intersect, we will get a 2 in the accumulator array If we have multiple lines in the image, we will get several local maxima in the accumulator array.

## Slide 8: Problem with the hough transform
Slope of the line -∞ ≤ a ≤ ∞. As the line becomes vertical, the slope approaches infinity. (a = tan(θ))
Large Accumulator
More memory and computation
Issue:
y = ax + b
Use other representation of a line:
ρ: the distance from the origin to the line.  Distance ρize of the image
θ: is the angle of the normal to the line with respect to the x-axis.  Orientation θ is finite: 0 ≤ θ <
Solution:
Image space
(x-y space)
Parameter space
(ρ-θ space)
Division of the ρ-θ-plane
into accumulator cells.

## Slide 9: Result
Original Image
Bilateral
Filter
CLAHE
Canny

## Slide 10: Result
Drawing result on canny edge image
Drawing result on original image
Result of Hough Transform with:
Distance resolution of the accumulator in pixels = 1
Angle resolution of the accumulator in radians = 180 (1 degree)
Threshold (Minimum number of votes (intersections in Hough accumulator) to consider a line) = 160

## Slide 11: Hough Transform: Circle Detection
Equation of circle:
a
b
r
x
y
=

## Slide 12: Hough Transform: Circle Detection
If radius r is know
Image space
Parameter space
=
x
y
=
, )
, )

## Slide 13: Using Gradient Information
Given edge location , ), Edge direction: θ = arctan
Image space
Parameter space
=
x
y
, )
θ
θ)
θ)

## Slide 14: Circle detection results
Original Image
Edge
Hough Transform
(a, b)
Hough Transform
(a, b)
r =
r =
Notes: Get high value over here but u get very strong value right here

## Slide 15: Hough Transform: Circle Detection with unknown radius
Image space
Parameter space

## Slide 16: Result
Edge
Drawing result on canny edge image
Drawing result on original image

## Slide 17: My function
dp: Inverse ratio of the accumulator resolution to the image resolution = 1.0
MinDist: Minimum distance between the centers of the detected circles. If the parameter is too small, multiple neighbor circles may be falsely detected in addition to a true one. If it is too large, some circles may be missed. = 5
Param1: parameter of Canny edge = 100
Param2: Threshold = 10
Min radius = 1
Max radius = 50

## Slide 18: HoughLines

## Slide 19: HoughCircles