## Slide 1: Timeline
DATE | TOPICS | RELATED TOPIC
05/5/2025 – 09/5/2025 | Basic transformations: Negative, Power Law, Log, Piecewise Linear stretching, Thresholding. Histogram analysis: Histogram Equalization, Histogram Matching, Contrast Local Adaptive Histogram Equalization. | Basic transformations & Histogram analysis
12/5/2025 - 16/5/2025 | Correlation and Convolution, Box filter, Gaussian Filter, Median filter. Resize images, Nearest Neighbor Interpolation, Linear Interpolation, Bilinear Interpolation. | Fundamentals of Spatial filtering
19/5/2025 – 21/5/2025 22/5/2025 – 23/5/2025 | Sobel filter: Derivative in detecting edge, Gradient, Sensitivity of derivatives to noise, Sobel Filter Program Bilateral filter: Compare Bilateral Filter and Gaussian Filter, My implementation program | Sobel filter Bilateral filter
26/5/2025 – 28/5/2025 29/5/2025 – 30/5/2025 | Canny edge detecting: Gradient, Non-Maximum Suppression, Hysteresis threshold, My implementation program Morphological Image Processing: Dilation, Erosion, Opening, Closing | Canny edge detecting, Morphological Image Processing
02/6/2025 – 04/6/2025 04/6/2025 – 06/06/2025 | Morphological Image Processing: Hit or miss transform, Boundary Extraction, Thinning, Skeleton. Thresholding | Morphological Image Processing Thresholding
09/6/2025 – 11/6/2025 12/6/2025 – 13/06/2025 | Template Matching Hough Transform: HoughLines, HoughCircle | Template Matching Hough Transform

## Slide 2: Timeline
DATE | TOPICS | RELATED TOPIC
16/6/2025 – 20/6/2025 | Geometric Transfrom | Geometric Transfrom

## Slide 3
GEOMETRIC TRANSFORM

## Slide 4: Image filtering
g(x) = h(f(x))
Image filtering: change the intensity range of image by considering its pixel value f(x) or neighboring pixel values to g(x).
Original Image
Result Image
h(f)
h(f)

## Slide 5: Geometric Mapping
g(x, y) = f(w(x, y))
Geometric Mapping : change domain of image coordinate, x by new coordinate w(x) by g(x) = f(w(x)).
Original Image
Result Image
w(x, y)
w(x)

## Slide 6: Example of Geometric warping

## Slide 7: 2x2 Linear Transformations
T(x, y)
T can represented by a matrix

## Slide 8: Forward mapping
Map each source pixel to a new position in the destination image
Map each destination pixel back to the corresponding point in source
T(u, v)
(x, y)
Pixel are missed
Inverse mapping
(x, y) often non-integer → Rounding to nearest pixel
(u, v) often non-integer → Need Interpolation in original image
May leave holes in destination image - Some pixels are missed
More complete and higher-quality result
R1(x, y) = Q11 · (x2 – x) / (x2 – x1) + Q21 · (x – x1) / (x2 – x1)
R2(x, y) = Q12 · (x2 – x) / (x2 – x1) + Q22 · (x – x1) / (x2 – x1)
P(x, y) = R1 · (y2 – y) / (y2 – y1) + R2 · (y – y1) / (y2 – y1)
Bilinear Interpolation

## Slide 9: Scaling (Stretching or Squishing)
S(u, v)
Forward:
(x, y)
Inverse:

## Slide 10: Rotation
Notes: Polar coordinate system

## Slide 11: Rotation
R(u, v)
Forward:
(x, y)
Inverse:

## Slide 12: Skewing
Original Image
Vertical Skew
Horizontal Skew

## Slide 13: Translation
T(u, v)
(x, y)
Problem: Translation can’t be expressed as 2x2 matrix
Forward:
Inverse:

## Slide 14: Homogenous Coordinates
The homogenous representation of a 2D point P(x, y) is a 3D point
With third coordinate is fictitious such that:
Find P from :
(With
In 3D coordinates system:

## Slide 15: Translation
T(u, v)
(x, y)
Forward:
Inverse:

## Slide 16: Scaling, Rotation
Scaling
Forward
Inverse
Rotation
Forward
Inverse
Skewing
Skew along the X-axis
Skew along the Y-axis

## Slide 17: Affine Transform
Affine transformation is a linear composite operation, as it merges all linear geometric transformations (such as rotation, scaling, shear, and reflection) along with translation into a single matrix operation.
Rotation, Scaling, Skewing
component
Translation
component
There are 6 parameters to be determined: , , , , , → Need at least 3 matching point pairs from the original and the transformed images.
Notes: The parallel lines remain parallel

## Slide 18: Perspective Transform
Camera obscura experiment
Plane
Plane
Point
Homography matrix

## Slide 19: Perspective Transform
The line from P(x, y, z) pass through the origin C(0, 0, 0) have equation:
To find the image point P', we intersect this line with the image plane z′ = f
Homogeneous coordinates form:
Or:
Projection matrix

## Slide 20: Perspective Transform
An interesting fact about the homography matrix is that it has a scale ambiguity. Since the input and output image coordinates are represented using homogeneous coordinates, you can multiply the homography matrix by any scalar k and the output image coordinates x2 and y2 will be unaffected. → We can normalize by setting a specific element to 1. → It has only 8 free parameters.
Example set to 1.
Notes: The parallel lines do not necessarily remain parallel

## Slide 21: Key Viewpoints of Perspective Transformation
A transformation to illustrate real 3D shape to 2D image plane
Parallel lines (that are not to parallel to the picture plane or not orthogonal to picture plane) converges to a Vanishing Point.
A straight line in 3D is also mapped to a straight line in 2D image.
Notes: The parallel lines do not necessarily remain parallel

## Slide 22: Image

## Slide 23: Perspective Transform
f
Image plane
x
y
z
Scene/ world point
Camera frame
Focal
length
C