## Slide 1: Timeline
DATE | TOPICS | RELATED TOPIC
23/6/2025 – 27/6/2025 | Setting up the development environment (Visual Studio, CUDA Toolkit, OpenCV, and other dependencies). Run the xvtCudaBatteryExample Calculate the maximum outer of lower part of the battery | 

## Slide 2
BATTERY INSPECTION PROJECT

## Slide 3: Battery inspection project
Cylinder battery
Image Source: Murashko, Kirill. "Thermal modelling of commercial lithium-ion batteries." (2016).
Xray-machine
Sample image (upper)
Separator (Jelly-Roll)
Negative pole
Positive pole
Sample image (lower)

## Slide 4: Goal of detection
Inspection Item:
① : Thickness of top cover
② : The inner diameter of the plant
③ : Distance between negative pole and positive pole.
④ : Number of NG negative pole (bent or tilted).
⑤ : Inclination angle of tilted poles.
⑥ : Maximum outer diameter
⑦ : The depth of the groove
⑧ : Distance between upper and lower edges.
Target:
Accurately measure internal linear distances between poles and Identify misaligned components
Challenge:
Input images have poor contrast
Shadow effect cause by Jelly Roll (separator)
Tab interference (in lower part)

## Slide 5: xvtBatteryExample to inspect Lower part

## Slide 6: Error code

## Slide 7: Inspection → Inspection2
Preprocessing
Contrast enhancement
Adjusts a selected ROI (Region of Interest) to ensure it remains inside an image.
Standardize the inspection process for both the lower and upper parts

## Slide 8: Inspection2
Apply gamma correction
Rotage image

## Slide 9: Find battery ROI

## Slide 10: Find battery ROI
Image before rotation
Image after rotation
Mirror ROI around center
Image(ROI)
Threshold
ROI
FindMaxContour

## Slide 11: Find battery ROI
Top-Left
Top-Right
boundingRect(contour)
Top-Left
Top-Right
Battery ROI
Battery ROI

## Slide 12: Check pole leaning
d
d
Pole Leaning detected position
Neglect Center region
Center of battery case
Affective range
"Pole Leaning Position” is the specific location in the image of the battery case where the poles are identified as leaning or deviating from their ideal positions.
After finding the Pole Leaning position, we can adjust the affective range (battery center/neglect region) to the new value.

## Slide 13: Find pole leaning (Auto)
ROI1
ROI2
ROI3
ROI1 | 
x1 | batteryROI.x
y1 | A2.y + JR ROI Y
width1 | batteryROI.width
height1 | Pole region height
ROI2 | 
x2 | x1 + padding
y2 | y1 + 2*padding
width2 | width1 – 2*padding
height2 | height1 – y2
Padding = battery width * 0.012
Step 1: Define ROI1 and ROI2 based on the specifications provided in Tables 1 and 2, respectively.
Step 2: Horizontal projection across ROI2 to detect sharp intensity variations. First, Sum each row (using cv::reduce with dim = 1) to get a 1D projection of changes across rows. Select the first valley of Derivative while scanning from bottom to top that satisfies the condition "prominence > 0.5. This point have sharp intensity variations help us to detect ROI3
Derivative

## Slide 14
ROI2
ROI3
Step 3: Divide the entire image into twelve equal sections. Determine the leftmost and rightmost boundaries for each section (typically visualized as red dashed lines).
Vertical projection of ROI3
limLeft
limRight
Valley(leaning position)
Peak (Leaning position)
Derivative
15
-15
Step 4: Check condition leaning:
  On the left side: valley is leaning line (index < limLeft && value < -15)
  On the right side: peak is leaning line (index > limRight && value > 15)

## Slide 15: Find pole leaning (Manual)
LimRight
LimLeft
Thd
Leaning position
Vertical projection of ROI3
ROI3
ROI1
ROI2
ROI3
ROI1 | 
x1 | batteryROI.x
y1 | A2.y + JR ROI Y
width1 | batteryROI.width
height1 | Pole region height
ROI2 | 
x2 | x1 + padding
y2 | y1 + 2*padding
width2 | width1 – 2*padding
height2 | height1 – y2
Step 1: Define ROI1 and ROI2 based on the specifications provided in Tables 1 and 2, respectively.
Padding = battery width * 0.012
Step 2: Apply CLAHE (Contrast Limited Adaptive Histogram Equalization) to the refined ROI3. Subsequently, perform vertical projection on the processed ROI3 to extract relevant information.
Step 3: Divide the refined ROI3 into twelve sections of equal size.
Step 4: Check condition leaning:
  Left leaning: Intensity previous column > thd & Intensity next column < thd
  Right leaning: Intensity previous column < thd & Intensity next column > thd
Leaning position

## Slide 16: Finding J/R position
ROI1
ROI4
ROI5
ROI6
ROI7
Step 1: Define ROI4 and ROI5 based on ROI1 and the "leaning" position information.
ROI4 | 
x4 | ROI1.x + leaning
y4 | ROI1.y
width4 | ROI1.width – 2 * leaning
height4 | ROI1.height
ROI5 | 
x5 | x4 + JR ROI X
y5 | y4
width5 | width4 – 2 * JR ROI X
height5 | height4
Step 2: Apply the multilevel Otsu thresholding method to ROI5 to determine an optimal threshold value. Utilize this threshold to create a binary image from ROI5.
Step 3: Identify contours within the binary image. Locate the largest contour to create ROI6 and employ moment analysis to calculate its center coordinates.
Step 4: Create ROI7 centered on the previously identified contour center with a window size of 40 pixels.
Step 5: Perform horizontal projection on ROI7. Identify the position where the projected value falls below half the window size 20. Additionally, locate the position with a projected value of zero (0).
center
window size
wdSize
wdSize/2
y-Axis
y-Axis
JR Top
JR Bottom
JR Bottom
JR Top

## Slide 17: Finding Cathode Line Position (Auto - Dijkstra-like algorithm)
neglect
Step 1: Applies local histogram equalization to the input image to enhance local contrast, making the cathode line more distinguishable.
Step 2: Applies a diagonal filter (custom edge enhancement) to the locally enhanced image to further highlight the cathode line.
Step 3: Calculates the start and end columns of the "center neglection area" (a region in the center of the image to be ignored, often because the center is not relevant or is noisy).
Step 4: Split Image into Left and Right Regions
Step 5: For each side, runs a Dijkstra-like algorithm to find the optimal path (the cathode line) from left to right and right to left.
Step 6: Merge Results

## Slide 18: A* algorithm
neglect
Step 1: Dynamic Programming Accumulation:
Look at the three possible positions in the previous column: directly above, same row, and directly below. Add the maximum value among these three to the current pixel. This accumulates the "best path" score to each pixel, favoring strong, continuous features.
Step 2: Traceback: Find the Best Path
Find the row with the maximum accumulated value in the last column (the end of the best path). Store this row index in vtLine for the last column.
For each previous column (right to left): In a window around the previous best row, find the row with the maximum value. If the maximum is not just the mean value (i.e., it's a real feature), use its index; otherwise, repeat the previous row.

## Slide 27
Nếu selectROI có tọa độ (x, y) và kích thước (width, height), thì: br (bottom right)